## Slide 1: Relief

## Slide 2: Information
Developing and Using Models
1. Patterns

## Slide 3: Relief
How would you show the relief of these landscapes on a map?
How many different ways can you think of to show relief?
Relief is the term geographers use to refer to the height and shape of the land.
Notes: Photo credits: both © 2018 JupiterImages Corporation

## Slide 4: How is relief shown on a map?
color shading.
spot heights
contour lines
Relief is shown on maps in three main ways:
10-20 m
21-30 m
31-40 m
41-50 m
19
31
21
37
46
32
14
12
10
20
30
40
Notes: This slide covers the Science and Engineering Practice:
Developing and Using Models: Develop, revise, and/or use a model based on evidence to illustrate and/or predict the relationships between systems or between components of a system.

## Slide 5: Ways to show relief
height in meters above sea level.
contour line – joins points of equal height.
spot height – represents the height of the land at a given point.
triangulation pillar – concrete post used by surveyors.
115
Notes: This slide covers the Science and Engineering Practice:
Developing and Using Models: Develop, revise, and/or use a model based on evidence to illustrate and/or predict the relationships between systems or between components of a system.

## Slide 6: Contours
Contours are lines that join points of equal height.
Relief is often shown on maps by light brown/orange lines known as contour lines.
Contour lines usually have a number attached to them. This number indicates height above sea level.

## Slide 7: Drawing contours
Notes: This slide covers the Science and Engineering Practice:
Developing and Using Models: Develop, revise, and/or use a model based on evidence to illustrate and/or predict the relationships between systems or between components of a system.

## Slide 8: Intervals
What height would points B and C be?
Contours are equally spaced in a vertical direction. The equal distances between the contours are called intervals.
Which point is 15 m high? A, B or C?
10
20
B
A could be at a height of 15 m.
A
How can you find out the height of a point between contours?
C
The intervals on this diagram are 10 m.
Notes: Teacher notes
In response to the questions, encourage students to estimate heights between contours.
There are no exact answers to the questions but you could discuss with the class what sensible estimates might be.

## Slide 9: Steep slopes and gentle slopes
Contours are useful. They tells us about the shape of the land without needing to see it.
When contours are close, the land is steep.
When contours are far apart, the slope is gentle.
20
30
40
50
60
10
0
10
Notes: Photo credits: both © FreeImages.com 2018

## Slide 10: Hills and valleys
Contours in this formation indicate a hill.
Contours in this formation indicate a river valley.
A map’s contour lines produce patterns that indicate particular landscape features:
Notes: Photo credits: both © FreeImages.com 2018

## Slide 11: Labeling landscapes
Notes: This slide covers the Science and Engineering Practice:
Developing and Using Models: Develop, revise, and/or use a model based on evidence to illustrate and/or predict the relationships between systems or between components of a system.

## Slide 12: Using color to show relief
Examine this satellite image of Mount Everest.
How can you tell which areas are higher than other areas?
The colors of the landscape produce a distinct pattern which helps us to understand the relief of the area.
snow line
river valley
green vegetation
barren rock
Notes: Photo credit: Courtesy of NASA

## Slide 13: Using color to show height on a map
Notes: This slide covers the Science and Engineering Practice:
Developing and Using Models: Develop, revise, and/or use a model based on evidence to illustrate and/or predict the relationships between systems or between components of a system.