## Slide 1: Moments

## Slide 2: Information
Developing and Using Models
Planning and Carrying Out Investigations
Using Mathematics and Computational Thinking
Constructing Explanations and Designing Solutions
2. Cause and Effect
3. Scale, Proportion, and Quantity
6. Structure and Function

## Slide 3: Rotational forces
A force, or a system of forces, can be used to make objects rotate around a pivot.
For example:
Applying a clockwise force to the wrench tightens the bolt.
Wheelchair athletes spin their wheels by pushing downwards.
Notes: Teacher notes
For more information about forces, please refer to the Introduction to Forces presentation.
Photo credits: wrench © PhotoMagicWorld, athlete © mezzotint, both at shutterstock.com 2018

## Slide 4: What is a moment?
When a force applied to an object makes it rotate around a pivot, the turning effect is called a moment.
The size of the moment depends on two factors.
The bigger the force, the larger the turning effect.
The greater the distance from the pivot to the point where the force is applied, the larger the turning effect.
Why does the door open more easily for the second person?
Notes: Teacher notes
The door opens more readily for the second person because the second person is applying a force further from the hinges of the door, which act as a pivot.
This slide covers the Science and Engineering Practice:
Developing and Using Models: Develop, revise, and/or use a model based on evidence to illustrate and/or predict the relationships between systems or between components of a system.

## Slide 5: Understanding moments
Notes: Teacher notes
This multiple choice quiz tests students’ understanding of the relationship between distance from pivot and moment of the force for five different examples, including; an Allen key, a door, a wrench, a screwdriver and a wheelbarrow.
This slide covers the Science and Engineering Practice:
Developing and Using Models: Develop, revise, and/or use a model based on evidence to illustrate and/or predict the relationships between systems or between components of a system.

## Slide 6: Calculating moments
The size of a moment can be calculated using the equation:
Distance (d) is the perpendicular distance from the pivot to the line of action of the force. It is measured in meters (m).
Force (F) is measured in newtons (N).
The moment of a force (M) is measured in newton meters (Nm).
moment of a force = force × distance
M = F × d
Notes: This slide covers the Science and Engineering Practice:
Using Mathematics and Computational Thinking: Use mathematical, computational, and/or algorithmic representations of phenomena or design solutions to describe and/or support claims and/or explanations.

## Slide 7: Calculating moments example (1)
A sleeping bat hangs from a branch. If the force of its weight is 8 N downwards and its perpendicular distance from the tree trunk is 20 cm, what is the moment of the force?
moment
moment of a force
= 1.6 Nm
= force × distance
= 8 × 0.2
Notes: This slide covers the Science and Engineering Practices:
Using Mathematics and Computational Thinking: Use mathematical, computational, and/or algorithmic representations of phenomena or design solutions to describe and/or support claims and/or explanations.
Using Mathematics and Computational Thinking: Apply techniques of algebra and functions to represent and solve scientific and engineering problems.
Photo credit: © Bird Hunter, shutterstock.com 2018

## Slide 8: Calculating moments example (2)
A wind turbine has blades that are 30 m long. The wind pushes against the tip of the top blade to create a moment of 150,000 Nm. What is the force of the wind?
force
moment of a force
moment
distance
150,000
30
force
force
= force × distance
=
=
= 5,000 N
Notes: This slide covers the Science and Engineering Practices:
Using Mathematics and Computational Thinking: Use mathematical, computational, and/or algorithmic representations of phenomena or design solutions to describe and/or support claims and/or explanations.
Using Mathematics and Computational Thinking: Apply techniques of algebra and functions to represent and solve scientific and engineering problems.

## Slide 9: Balanced and unbalanced forces
When forces in opposite directions have the same value, they cancel each other out. We say that the forces are balanced.
If the forces on an object are not balanced, there is a resultant force, and the object accelerates.
The object either remains stationary or continues to move at a constant speed.
Notes: Teacher notes
For more information about balanced and unbalanced forces, please refer to the Acceleration, Newton’s First Law of Motion, Newton’s Second Law of Motion and Resultant Forces presentations.

## Slide 10: Clockwise and counterclockwise moments (1)
When Johannes and Victor lift their feet off the ground, what will happen to the seesaw?
The force of gravity acting on each person creates a turning effect on the seesaw. It creates an clockwise moment on Victor. On Johannes, it creates a counterclockwise moment.
Victor
Johannes
pivot point
Notes: This slide covers the Science and Engineering Practice:
Constructing Explanations and Designing Solutions: Apply scientific ideas, principles, and/or evidence to provide an explanation of phenomena and solve design problems, taking into account possible unanticipated effects.

## Slide 11: Clockwise and counterclockwise moments (2)
The clockwise moment is larger than the counterclockwise moment, so the seesaw will turn in a clockwise direction. The seesaw tips and Victor is lifted into the air.
When Johannes and Victor lift their feet off the ground, what will happen to the seesaw?
Victor
Johannes
Notes: This slide covers the Science and Engineering Practice:
Constructing Explanations and Designing Solutions: Apply scientific ideas, principles, and/or evidence to provide an explanation of phenomena and solve design problems, taking into account possible unanticipated effects.

## Slide 12: Balancing moments
If an object is balanced about a pivot, then we can say that:
sum of counter- clockwise moments
sum of clockwise moments
=
What would happen if Victor sat on the seesaw with someone the same weight as him?
They would each exert the same downward force. Since they are sitting the same distance away from the pivot, their moments are equal and the seesaw is balanced.
Notes: This slide covers the Science and Engineering Practice:
Constructing Explanations and Designing Solutions: Apply scientific ideas, principles, and/or evidence to provide an explanation of phenomena and solve design problems, taking into account possible unanticipated effects.

## Slide 13: Balancing scales
Notes: Teacher notes
This activity tests pupils’ understanding of both the moment equation and how to balance moments. Set up a combination of weights on the left-hand side of the scales and ask pupils to work out what to add to the right-hand side to balance the scales. Pupils could also be asked to think of as many different solutions as possible to each problem.
Arrangements of weights on the left (and some possible answers) might include:
400 g at 10 cm (400 g at 10 cm; 200 g at 20 cm; 800 g at 5 cm)
100 g at 17 cm (100 g at 17 cm is the only solution)
700 g at 20 cm (using all four hooks: 600 g at 10 cm with 400 g at 20 cm; 1000 g at 12 cm with 100 g at 20 cm)
100 g at 20 cm, 12 cm and 6 cm (200 g at 19 cm is the only solution)
This slide covers the Science and Engineering Practice:
Planning and Carrying Out Investigations: Make directional hypotheses that specify what happens to a dependent variable when an independent variable is manipulated.

## Slide 14: Calculating forces and distances

## Slide 15: Lifting heavy objects (1)
The explorer Jane Wolf needs to move a 1,000 N boulder that is blocking an entrance. She can only apply a 20 N force, but she also has a 6 m metal pole.
How can Jane use moments to move the boulder?
1,000 N
6 m
Jane uses the smaller stone as a fulcrum, or a pivot point, and the metal pole as a lever.
To see why this works, we need to calculate the clockwise and counterclockwise moments around the stone.

## Slide 16: Lifting heavy objects (2)
How can Jane use moments to move the boulder?
The smaller stone is 0.1m from the boulder, which exerts a 1,000 N force downwards.
Calculate the counterclockwise moment the boulder creates.
= 1,000 × 0.1
moment of a force = force × distance
= 100 Nm
100 Nm
Notes: Teacher notes
For simplicity, it is assumed that the weight of the boulder acts as a single downwards force at the end of the pole, with a perpendicular distance of 0.1 m from the pivot point.
This slide covers the Science and Engineering Practice:
Using Mathematics and Computational Thinking: Apply techniques of algebra and functions to represent and solve scientific and engineering problems.

## Slide 17: Lifting heavy objects (3)
How can Jane use moments to move the boulder?
Jane applies a downwards force of 20 N to her end of the lever, at a perpendicular distance of 5.9 m from the stone.
Calculate the clockwise moment created by Jane.
= 20 × 5.9
moment of a force = force × distance
= 118 Nm
100 Nm
118 Nm
Notes: Teacher notes
Again, for simplicity, it is assumed that Jane applies a single downwards force at her end of the pole, with a perpendicular distance of 5.9 m from the pivot point.
This slide covers the Science and Engineering Practice:
Using Mathematics and Computational Thinking: Apply techniques of algebra and functions to represent and solve scientific and engineering problems.

## Slide 18: Lifting heavy objects (4)
How can Jane use moments to move the boulder?
The clockwise moment on the lever is greater than the counterclockwise moment on the lever.
100 Nm
118 Nm
The forces are unbalanced, and the lever rotates around the pivot, lifting the boulder.

## Slide 19: Levers
Jane was able to move the boulder because she used a lever. Levers are designed to transmit the rotational effects of forces in order to make it easier to lift objects.
To lift the load, an upwards force is applied.
Another example of a mechanical system that uses a lever is a wheelbarrow.
fulcrum
load
On a wheelbarrow, the center of the wheel is the fulcrum. The object to be lifted is called the load.

## Slide 20: Gears
Gears, like levers, are also used to transmit the rotational effects of forces.
Gears can be used to:
change the direction of rotation
convert from rotational to linear motion
Notes: Teacher notes
The image on the left is a bevel gear mechanism in which a clockwise motion in the vertical plane is transformed into an counterclockwise motion in the horizontal plane. The image on the right is a rack and pin system. To extend this slide, ask students to come up with their own gear configurations and to describe the transformation of movement they create.
Gears can also be used to change the speed and power of a movement.

## Slide 21: How do bicycle gears work?
Notes: This slide covers the Science and Engineering Practice:
Constructing Explanations and Designing Solutions: Apply scientific ideas, principles, and/or evidence to provide an explanation of phenomena and solve design problems, taking into account possible unanticipated effects.